## Slide 1: Metric Via Fanout BGA’s
The following slides provide Via Fanout routing examples for various pitch
Ball Grid Array Packages

## Slide 2: Presented By: Tom Hausherr Director of Technology Tom.@PCBLibraries.com

## Slide 3
100 PIN 0.8mm PITCH BGA
Via Data
Pad: 0.45 (18)
Hole: 0.2 (8)
Anti-Pad: 0.65 (26)
BGA Pad Size: 0.4 (16)
Trace/Space Data
Trace Width: 0.1 (4)
Trace/Trace Space: .1
Trace/Via Space: .125
Routing Grid: 0.1 (4)
Via Grid: 0.2 (8)
Part Place Grid: 1 (40)

## Slide 4
100 PIN 0.8mm PITCH BGA
Via Data
Pad: 0.45 (18)
Hole: 0.2 (8)
Anti-Pad: 0.65 (26)
BGA Pad Size: 0.4 (16)
Trace/Space Data
Trace Width: 0.125 (5)
Trace/Trace Space: .125
Trace/Via Space: 0.1 (4)
Routing Grid: 0.05 (2)
Via Grid: 0.2 (8)
Part Place Grid: 1 (40)

## Slide 5
100 PIN 1mm PITCH BGA
Via Data
Pad: 0.50 (20)
Hole: 0.25 (10)
Anti-Pad: 0.70 (28)
BGA Pad Size: 0.5 (20)
Trace/Space Data
Trace Width: 0.1 (4)
Trace/Trace Space: 0.1
Trace/Via Space: 0.1
Routing Grid: 0.1 (4)
Via Grid: 1 (40)
Part Place Grid: 0.5 (20)

## Slide 6
100 PIN 1mm PITCH BGA
Via Data
Pad: 0.55 (22)
Hole: 0.25 (10)
Anti-Pad: 0.75 (30)
BGA Pad Size: 0.5 (20)
Trace/Space Data
Trace Width: 0.125 (5)
Trace/Trace Space: 0.125
Trace/Via Space: 0.16 (6)
Routing Grid: 0.05 (2)
Via Grid: 1 (40)
Part Place Grid: 0.5 (20)

## Slide 7
100 PIN 1mm PITCH BGA
Via Data
Pad: 0.55 (22)
Hole: 0.25 (10)
Anti-Pad: 0.75 (28)
BGA Pad Size: 0.5 (20)
Trace/Space Data
Trace Width: 0.15 (6)
Trace/Trace Space:0.15
Trace/Via Space: 0.15
Routing Grid: 0.1 (4)
Via Grid: 1 (40)
Part Place Grid: 0.5 (20)

## Slide 8
100 PIN 1mm PITCH BGA
Via Data
Pad: 0.50 (20)
Hole: 0.25 (10)
Anti-Pad: 0.70 (28)
BGA Pad Size: 0.5 (20)
Trace/Space Data
Trace Width: 0.2 (8)
Trace/Trace Space: 0.2
Trace/Via Space: 0.15
Routing Grid: 0.1 (4)
Via Grid: 1 (40)
Part Place Grid: 0.5 (20)

## Slide 9
100 PIN 1.27mm PITCH BGA
Via Data
Pad: 0.635 (25)
Hole: 0.30 (12)
Anti-Pad: 0.85 (33)
BGA Pad Size: 0.6 (24)
Trace/Space Data
Trace Width: 0.127 (5)
Trace/Trace Space:.127
Trace/Via Space: 0.127
Routing Grid: 0.127 (5)
Via Grid: 0.635 (25)
Part Place Grid 1: 1.27
Part Place Grid 2: 0.635

## Slide 10
100 PIN 1.5mm PITCH BGA
Via Data
Pad: 0.55 (22)
Hole: 0.25 (10)
Anti-Pad: 0.75 (30)
BGA Pad Size: 0.75
Trace/Space Data
Trace Width: 0.1 (4)
Trace/Trace Space: 0.1
Trace/Via Space: 0.1
Routing Grid: 0.05 (2)
Via Grid: 0.5 (20)
Part Place Grid: 1 (40)

## Slide 11
100 PIN 1.5mm PITCH BGA
Via Data
Pad: 0.6 (24)
Hole: 0.25 (10)
Anti-Pad: 0.8 (32)
BGA Pad Size: 0.75
Trace/Space Data
Trace Width: 0.125 (5)
Trace/Trace Space: 0.125
Trace/Via Space: 0.125
Routing Grid: 0.25 (10)
Via Grid: 0.5 (20)
Part Place Grid: 1 (40)

## Slide 12
100 PIN 1.5mm PITCH BGA
Via Data
Pad: 0.55 (22)
Hole: 0.25 (10)
Anti-Pad: 0.75 (28)
BGA Pad Size: 0.75
Trace/Space Data
Trace Width: 0.15 (6)
Trace/Trace Space:0.15
Trace/Via Space: 0.15
Routing Grid: 0.1 (4)
Via Grid: 0.5 (20)
Part Place Grid: 1 (40)

## Slide 13
100 PIN 1.5mm PITCH BGA
Via Data
Pad: 0.60 (24)
Hole: 0.25 (10)
Anti-Pad: 0.80 (32)
BGA Pad Size: 0.75
Trace/Space Data
Trace Width: 0.2 (8)
Trace/Trace Space: 0.2
Trace/Via Space: 0.15
Routing Grid: 0.1 (4)
Via Grid: 0.5 (20)
Part Place Grid: 1 (40)

## Slide 14: Metric BGA Working Grids
Placement, Via Fanout and Routing grids should be evenly divisible into 1mm
Metric Working Grids
1
0.5
0.25
0.2
0.125
0.1
0.05
Metric Non-Working Grids
0.9
0.8
0.7
0.6
0.4
0.3
0.15

## Slide 15: Part Placement & Via Fanout
When placing components on a PCB Design, always have your Via Display Grid turned on.
When you place the parts, place the part pins evenly in-between your Via Display Grid to optimize the via fanout lengths and maximize your available routing channels.
You may have to use various placement grids to accomplish this, but you will enhance the routing phase of the PCB Design layout.

## Slide 16: Optimal Via Padstacks
0.1 Trace Width / 0.1 Route Grid
Pad Size: 0.5
Hole Size: 0.25
Anti-pad: 0.7 – Avoid Trace / Anti-pad Overlap
0.125 Trace Width / 0.25 Route Grid
Pad Size: 0.65
Hole Size: 0.3
Anti-pad: 0.8 – Avoid Trace / Anti-pad Overlap
0.15 Trace Width / 0.1 Route Grid
Pad Size: 0.55
Hole Size: 0.25
Anti-pad: 0.75 – Avoid Trace / Anti-pad Overlap

## Slide 17: Maximize Routing Channels
Design your PCB like you are planning a housing development
First establish where all the freeways are going to go – Buss Routes and Main Arteries
Then establish the local road map – Trace Routes that don’t have to bend
Then build the houses along each side of the local roads – Via Sites

## Slide 18: Questions?