## Slide 1: The G0 experiment at JLAB
Forward and backward angle PV e-p elastic and e-d (quasielastic) in JLab Hall C
superconducting toroidal magnet
scattered particles detected in segmented scintillator arrays in spectrometer focal plane
custom electronics count and process scattered particles
at > 1 MHz
first engineering run 2002
first data taking 2003

## Slide 2: G0 elastic scattering program
8.41
7.07
13.13
-34.00
Ad
6.96
31.41
16.10
-25.01
AB
1.01
18.63
51.80
-13.77
AF
(ppm)
(ppm)
(ppm)
(ppm)
at Q2 = 0.44 (GeV/c)2
AF : one measurement for all Q2  detect recoil protons
AB : three measurements for three Q2 values:  detect electrons at 108°
Ad : Quasielastic scattering (x3) from deuterium  detect electrons at 108°

## Slide 3: G0 Apparatus
One octant’s scintillator array
20 cm LH2 Target

## Slide 4
G0 Detection Scheme
Detect scattered Protons:
Magnet sorts protons by Q2
at one setting
Beam bunches 32 nsec apart
Flight time separates p and 
detector
module
Beam spin flipped every 30 ms: 

## Slide 5: FR TOF Spectra

## Slide 6: G0 Fall 02 Engineering Run
Complete detector checkout:
magnet operational and stable at full current (5000 Amps)
LH2 target operation very smooth, density fluctuations negligible
detailed studies of detector gains, etc.
photon background rates initially high, now shielded
electronics, DAQ, generally working well, deadtime studies underway.
Beam checkout:
40 A achieved but not stable
10 C of detector asymmetry data acquired at 30 uA in Jan ‘ 03.
Goals achieved for “noise” specifications on beam at 15 Hz:
position stability: 20 
energy stability: 0.00033%
current stability: 200 ppm
Helicity-correlated beam feedback systems tested:
charge asymmetry easily controlled to < few ppm
Position feedback needs work

## Slide 7: Deadtime Studies
With intensity feedback, can induce large charge asymmetry.
Any uncorrected deadtime will induce detector asymmetry.
Works if beam charge asymmetry uncorrelated with beam position differences
Analysis in progress
Slope = 3-6% w/ 15 A beam current
Small fraction from charge/position correlation

## Slide 8: On-line Asymmetries at 4500 Amps
10 hours of beam at 15 A, reduced magnet current.
4 days asymmetry data at 5000 Amps and 30 A on disk, analysis in progress

## Slide 9: G0 Backward Angle
Electron detection: one Q2 per magnet setting:  = 108°
Add Cryostat Exit detectors to define electron trajectory
1 scaler per channel FPD/CED pair
Deuterium: pion rejection required 
aerogel Cerenkov detector (Caltech, TRIUMF, Grenoble)
Ebeam | /e ratio | 
(MeV) | H | D
424 | 0.01 | 0.4
585 | 0.04 | 1.0
799 | 0.4 | 11.4
(J. Martin, Caltech)

## Slide 10: G0 Experiment Schedule
Forward angle
  First commissioning completed (Oct ’02-Jan ’03)
  Beam request for 2nd commissioning and physics scheduled for fall ’03
Backward angle
  Approved by PAC Jul ‘01
  If forward angle successful, will be ready for turnaround and physics late ’04
  2nd, 3rd Q2 points not yet submitted to PAC
This work had been jointly supported by Dept of Energy
And National Science Foundation

## Slide 12: G0 expected uncertainties